## Slide 1: Sensing Soft Robot Shape Using Electrical Impedance Tomography
MRes thesis presentation
Charlie DeLorey
07/09/2021

## Slide 2: This slide will be removed for the actual presentation, I have it here for reference
Abstract
Intro and literature review
  Problem statement
  State of robotics: soft vs rigid
  Sensors and soft robots (grippers)
  Control schemes for soft robots
  Electrical impedance tomography (EIT)
  Chronology of my project (simulations, silicone, hydraulic, back to silicone, data, ML, analysis and writeup)
  Aims and objectives (showing a working moving soft finger that can be accurately sensed with my EIT setup to a satisfactory state)
Methodology
  Integrated 3D printed hydraulic finger
  SDM silicone cable-actuated finger
  EIT chamber (side sections, maybe even take a picture of a cut up actuator)
  Actuation (cable+stepper motor, Arduino)
  Data acquisition (DAQ, electrodes, serial connection, webcam)
  Software (data processing and alignment, probably some filtering for EIT data,)
  Experimental setup/protocol (e.g. finger actuated 5 times, ..., finger comes in contact with object _____, ...)
Results
  EIT voltage data vs cable pull length data
  EIT+cable data vs ground truth camera data (get performance error)
  T: Perhaps a full EIT image of the chamber in varying states of actuation
  ML function learning performance/accuracy
  Conclusion and discussion (a little bit)
Discussion
  Conclusions and summary of my results
  Future work:
    How would I fix the problems I stated above
    Assuming I fix my problems, what would I do with this (full grasper, add fingertips, what applications that would have, ...)
      discussion off of being able to get an EIT image from my finger
  Conclusion (if I have time), “I made this it does this it’s great”
References

## Slide 3: Introduction and Objectives
Sensing complications in soft robotics
  Soft robots are difficult to model due to their near infinite degrees of freedom from their compliant nature
  Rigid sensors would inhibit this compliant nature, preventing normal function
Proposed solution
  A flexible soft sensor system that can detect soft robot actuation without impinging on normal movement

## Slide 4: Methodology
EIDORS
Hydraulic actuator
SDM actuator
EIT data
Computer vision

## Slide 5: Methodology – EIDORS Simulations
EIDORS¹ is an open-source software for simulating EIT signals
Current sources and reading points are electrodes, placed on a volume
No bend
Single bend
Two bends
[1]: Andy Adler, William R B Lionheart (2006) "Uses and abuses of EIDORS: An extensible software base for EIT", Physiol. Meas. 27:S25-S42, 2006
(a)
(b)
(c)

## Slide 6: Methodology – EIDORS PneuNet simulations
No bend
Primary bend
Secondary bend
Primary bend with inflation
Consequent bending shows more activity along the main chamber and electrodes
Indicates placing electrodes close to bend points is beneficial
(a)
(b)
(c)
(d)

## Slide 7: Methodology – EIT
SDM actuator incremental flexing
Voltage signal is the result of the changing path length between electrodes within a conductive medium (0.5% saline solution)
As the path length increases, the resistivity increases
Relationship described by , where
R = resistivity
ρ = resistance
L = path length
A = cross-sectional area
SDM actuator flexing (5 iterations)

## Slide 8: Methodology – Hydraulic actuator
Two-in-one hydraulic actuation chamber and EIT chamber
Bellows design allows smaller chambers to inflate, resulting in a bend
Issues:
  3D printed material not watertight, making data inaccurate
  Thickness of material prevented easy actuation
  Needed high pressure to actuate
(a)
(b)
(c)
(d)

## Slide 9: Methodology – 2-chamber pneumatic actuator
Separated EIT (liquid) and actuation (air) chambers
Frequent leaking due to imperfect 3D print, like previous iteration
Actuation chamber/bellows
EIT chamber
Electrodes
(a)
(b)
(c)

## Slide 10: Methodology – SDM cable-driven actuator
0.5x speed
(a)
(b)
(d)
Shape deposition modelling (SDM) cable-driven finger design
EIT chamber placed anterior running lengthwise along the finger
Cable drive provides reliable and measurable actuation with a simple design
EIT chamber
Electrodes
EIT chamber
EIT chamber
Electrodes
(c)

## Slide 11: Methodology – Point tracking
OpenCV methods used to track markers along actuator
Derived bending angle of soft robot finger
Synchronisation of video with data done with blue LED in frame
Pixels
ArUco marker tracking
Optical flow tracking
(a)
(b)
(c)

## Slide 12: Results – Finger actuation
Physical performance of SDM actuator
**Here I am going to add an image or two of me testing the physical limits of the actuator, max bend angle, it moving something of particular mass, etc

## Slide 13: Results – EIT data with actuator bending
EIT signal change nonlinearly as bending angle increases
EIT signals of joints change when finger is actuated
Voltages against SDM actuator cable pull distance
Bending angle with measured voltage by joint
Time (samples)

## Slide 14: Discussion
While some materials are compliant or could be considered “soft”, they are not all suitable to work with a fluid-actuated system
A simple 6-electrode EIT chamber was added to a soft robot actuator and could provide sensing signals as to the shape change of the actuator
As soft robots are naturally compliant and flexible, using a similarly soft sensor still allows the robot to move freely
Future work includes:
  Advanced ML techniques applied to large data sets
  Develop chamber with more electrodes to acquire more detailed sensor data (using an FPC)
  Assemble multiple fingers together to create a grasper, and evaluate the performance of the fingers on grasping and object recognition tasks (from EIT data alone)

## Slide 15: References
References to be inserted

## Slide 16: Questions?

## Slide 17: Appendix A
I think it would be a good idea to put in some additional images/text, in case anyone asks about things I’m not already presenting on. This will be added today